## Slide 1: Smart Dustbin with Dry and Wet waste segregation
Submitted by:
Mohit Manhas (12214162)(35)
Anubhav Singh (12208856)(13)
Ayush Agarwal : (12208628)(9)
Vishal Kumar : (12213669)(26)
Anjani Kumara (12215346)(36)
Guided By:
Dr. Deepika Ghai

## Slide 2: Introduction
Rapid urbanization has led to increased waste generation, creating challenges in efficient waste management. Effective segregation of dry (paper, plastic) and wet (food, organic) waste is crucial for recycling, reducing landfill use, and minimizing environmental impact. However, manual segregation is often inefficient and prone to errors.
The "Smart Dustbin with Dry and Wet Waste Segregation" automates waste sorting using sensors and microcontrollers, directing each type of waste into separate compartments. Equipped with distance sensors, moisture sensors, and servo motors, the system ensures accurate waste classification and convenient disposal. Through IoT integration with Blynk, it enables real-time waste level monitoring and sends alerts when bins are full, supporting cleaner, more sustainable urban spaces.

## Slide 3: Applications of Project Topic
Smart Dustbin with Dry and Wet waste segregation
Households
Hospitals and Clinics
Agricultural Farms
Public Spaces

## Slide 4: Library used in Project
RPi.GPIO: Used for GPIO pin control on the Raspberry Pi, allowing interaction with various sensors, servo, and other hardware components.
time: Provides time-related functions, such as delays and timestamps.
smtplib: Used to handle sending emails via SMTP (Simple Mail Transfer Protocol).
email.mime.text (specifically MIMEText): Part of the email package, used to create text-based email messages.
RPLCD.i2c: Provides support for controlling LCD displays via I2C on the Raspberry Pi, allowing text to be displayed on the screen.
blynklib: Blynk library to interact with the Blynk IoT platform, enabling remote monitoring and control of device data.

## Slide 5: Working of Project
Step 1: Explain in 2 lines
INPUT of STEP1
OUPUT w.r.t STEP1

## Slide 6
Step 2: Explain in 2 lines
INPUT of STEP2
OUPUT w.r.t STEP2

## Slide 7
Step 3: Explain in 2 lines
INPUT of STEP3
OUPUT w.r.t STEP3

## Slide 8
Step 4: Explain in 2 lines and so on steps
INPUT of STEP4
OUPUT w.r.t STEP4

## Slide 9: Complete Process of Project Working
Input Detection
Waste Identification
Segregation Mechanism Activation
Waste Disposal
Status Indication and Reset

## Slide 10: Conclusion
Efficient Waste Management: Automates dry and wet waste
segregation, reducing manual sorting.
Environmental Impact: Supports recycling and composting, reducing
landfill waste and promoting eco-friendly practices.
User Convenience: Simplifies disposal and encourages responsible
habits.
Scalability: Adaptable for homes, public spaces, offices, and industries.
Cost-Effective: Uses affordable components for economical waste
segregation.
Smart City Initiative: Enhances urban cleanliness and sustainability.
Educational Value: Demonstrates technology’s role in tackling
environmental issues and promoting sustainability.

## Slide 11: Project Video

## Slide 12: Future Scope
Smart Dustbin with Dry and Wet waste segregation
Integration with IoT:
Data Analytics
Advanced Sensors for Enhanced Sorting
Mobile App Integration

## Slide 13: References
[1] Helen, R., Karthika, P., Selvakumar, R., & Thenmozhi, T. (2022, January). Smart bin and intelligent waste segregator using IoT. In 2022 4th International Conference on Smart Systems and Inventive Technology (ICSSIT) (pp. 125-131). IEEE.
[2] Mahajan, K., & Chitode, J. S. (2014). Waste bin monitoring system using integrated technologies. International Journal of Innovative Research in Science, Engineering and Technology, 3(7).
[3] Bhattacharya, D., & Reshmi, W. (2013, December). Analysis and design of an embedded environment informer for waste disposal cleaning. In 2013 International Conference on Green Computing, Communication and Conservation of Energy (ICGCE) (pp. 419-422). IEEE.
[4] Navghane, S. S., Killedar, M. S., & Rohokale, V. M. (2016). IoT based smart garbage and waste collection bin. International Journal of Advanced Research in Electronics and Communication Engineering (IJARECE), 5(5), 1576-1578.
[5] Anjanappa, C., Parameshwara, S., Vishwanath, M. K., Shrimali, M., & Ashwini, C. (2022). AI and IoT based garbage classification for the smart city using ESP32 cam. International Journal of Health Sciences, (III), 4575-4585.

## Slide 14: Appendix
import RPi.GPIO as GPIO
import time
import smtplib
from email.mime.text import MIMEText
from RPLCD.i2c import CharLCD
from time import sleep
import blynklib
# LCD Settings
I2C_ADDR = 0x27 # I2C address for your LCD (adjust if necessary)
LCD_WIDTH = 16
LCD_HEIGHT = 2
lcd = CharLCD('PCF8574', I2C_ADDR, cols=LCD_WIDTH, rows=LCD_HEIGHT)
# Email Settings
SENDER_EMAIL = 'ssjover9000123@gmail.com'
SENDER_NAME = 'Raspberry Pi'
SENDER_PASSWORD = 'sise qhiq disj znyl' # Make sure to keep this secure
RECIPIENT_EMAIL = 'mohitd2004@gmail.com'
EMAIL_SUBJECT = 'Alert'
# GPIO Pins
SERVO_PIN = 15
D_TRIGGER_PIN = 19
D_ECHO_PIN = 18
W_TRIGGER_PIN = 12
W_ECHO_PIN = 13
IR_SENSOR_PIN = 26
SOIL_PIN = 4 # Digital soil moisture sensor connected to GPIO 4
# Blynk Settings
BLYNK_AUTH_TOKEN = "4WLYv3MoesdlDoxo540VYLucEHSPeyxm"
blynk = blynklib.Blynk(BLYNK_AUTH_TOKEN)
# Setup GPIO and Servo
GPIO.setmode(GPIO.BCM)
GPIO.setup(SERVO_PIN, GPIO.OUT)
servo = GPIO.PWM(SERVO_PIN, 50)
servo.start(0)
GPIO.setup(D_TRIGGER_PIN, GPIO.OUT)
GPIO.setup(D_ECHO_PIN, GPIO.IN)
GPIO.setup(W_TRIGGER_PIN, GPIO.OUT)
GPIO.setup(W_ECHO_PIN, GPIO.IN)
GPIO.setup(IR_SENSOR_PIN, GPIO.IN)
GPIO.setup(SOIL_PIN, GPIO.IN) # Setup soil moisture sensor as input

## Slide 15
def move_servo(angle):
duty = angle / 18 + 2
GPIO.output(SERVO_PIN, True)
servo.ChangeDutyCycle(duty)
sleep(0.5)
GPIO.output(SERVO_PIN, False)
servo.ChangeDutyCycle(0)
def measure_distance(trigger_pin, echo_pin):
GPIO.output(trigger_pin, False)
sleep(0.2)
GPIO.output(trigger_pin, True)
time.sleep(0.00001)
GPIO.output(trigger_pin, False)
start_time = time.time()
stop_time = time.time()
while GPIO.input(echo_pin) == 0:
start_time = time.time()
while GPIO.input(echo_pin) == 1:
stop_time = time.time()
time_elapsed = stop_time - start_time
distance = (time_elapsed * 34300) / 2 # Distance in cm
return distance
def send_email(message):
smtp = smtplib.SMTP_SSL('smtp.gmail.com', 465)
smtp.login(SENDER_EMAIL, SENDER_PASSWORD)
msg = MIMEText(message)
msg['Subject'] = EMAIL_SUBJECT
msg['From'] = SENDER_NAME
msg['To'] = RECIPIENT_EMAIL
smtp.sendmail(SENDER_EMAIL, RECIPIENT_EMAIL, msg.as_string())
smtp.quit()
# Main Loop
try:
while True:
blynk.run() # Run the Blynk event handler
# Measure distances
wet_distance = measure_distance(W_TRIGGER_PIN, W_ECHO_PIN)
dry_distance = measure_distance(D_TRIGGER_PIN, D_ECHO_PIN)
h = 20 # Height of the bin (adjust as necessary)
dry_level = int(((h - (dry_distance - 7)) / h) * 100)
wet_level = int(((h - (wet_distance - 6)) / h) * 100)
# Send data to Blynk
blynk.virtual_write(0, dry_level)
blynk.virtual_write(1, wet_level)
# Display levels on LCD
lcd.clear()
lcd.write_string(f"Wet Waste: {wet_level}%")
lcd.cursor_pos = (1, 0)
lcd.write_string(f"Dry Waste: {dry_level}%")
# Garbage detection and sorting logic
if GPIO.input(IR_SENSOR_PIN) == 0:
moisture = GPIO.input(SOIL_PIN) # Reading digital soil moisture
if moisture == GPIO.LOW and wet_level < 90: # Wet garbage detected
lcd.clear()
lcd.write_string("Wet Garbage")
lcd.cursor_pos = (1, 0)
lcd.write_string("Detected")
move_servo(20)
sleep(2)
move_servo(70)
elif moisture == GPIO.HIGH and dry_level < 90: # Dry garbage detected
lcd.clear()
lcd.write_string("Dry Garbage")
lcd.cursor_pos = (1, 0)
lcd.write_string("Detected")
move_servo(120)
sleep(2)
move_servo(70)
elif moisture == GPIO.LOW and wet_level >= 90: # Wet bin full
lcd.clear()
lcd.write_string("Wet Garbage")
lcd.cursor_pos = (1, 0)
lcd.write_string("Is Full")
send_email("Wet Garbage is Full")
elif moisture == GPIO.HIGH and dry_level >= 90: # Dry bin full
lcd.clear()
lcd.write_string("Dry Garbage")
lcd.cursor_pos = (1, 0)
lcd.write_string("Is Full")
send_email("Dry Garbage is Full")
sleep(1)

## Slide 16
except KeyboardInterrupt:
print("Program stopped by user")
finally:
GPIO.cleanup()
servo.stop()
lcd.close()